Q25 SLAB/ BRICK/ SETT/ COBBLE PAVINGS

215 CONCRETE FLAG PAVING

Aggregate Industries is a supplier of hard landscaping products to the UK construction industry. Click on the name below to jump to the product and specification details.

Eco Paving

StoneMaster Paving

Andover Paving

Appalachian Paving

Ultrapave Paving

Moordale Paving

Courtstone Paving

Academy Paving

British Standard Paving

Tactile Paving

Elite Format 3 Paving

Eco Paving
The Eco Range has been developed to make a positive contribution to sustainable construction by maximising resource productivity.

The factory utilises advanced equipment to meet high environmental standards.

The range of EcoPave and EcoKerb products uses secondary and recycled materials in the manufacture of it’s precast concrete units. The only virgin resource used in the product is cement and even this has been partially substituted with recycled materials. 
The pavings comply with the strength and slip resistant requirements of BS EN 1339.
Slip Resistance to BS EN 1339:Low.

Ecopave: Size: Textured finish - 400 x 400 x 65mm / 450 x 450 x 70mm / 600 x 600 x 50mm /400x200x65mm 
Ground finish - 400 x 400 x 65mm / 450 x 450 x 70mm / 600 x 600 x 50mm
Consult with the technical literature for details. We also provide a design and specification service and it is recommended that they are consulted early in the design process.

Manufacturer: Aggregate Industries, Hulland Ward, Ashbourne, Derbyshire DE6 3ET. Tel: 01335 372222. Fax: 01335 370074 Web: http://www.aggregate.com/commercial-hard-landscaping

Product reference: EcoPave
Colour/ Finish: Eco Grey Fleck,  Eco Buff Fleck
Finish: Textured / Ground
Method of manufacture: Hydraulically pressed 
Nominal sizes:
400 x 400 x 65mm / 450 x 450 x 70mm / 600 x 600 x 50mm / 400x200x65 – for Textured finish – Both Colours

Ground Finish – Grey Fleck only
NB – Buff Fleck Textured made to order

StoneMaster Paving 
A premium quality paving range manufactured to simulate the aesthetic appearance of natural sandstone. Stonemaster is manufactured with up to 50% reclaimed/recycled content.
The slabs are semi dry pressed and secondary processed. Slabs include pre-treatment to protect against surface contamination.
The paving is designed for high volume pedestrian areas, town centres, shopping precincts, footway crossings and for areas subject to occasional light vehicular overrun.
Stonemaster products comply with the strength and slip resistant requirements of BS EN 1339. 
Slip Resistance to BS EN 1339: Low.

StoneMaster : Size: 600 x 450mm / 450 x 450mm / 450 x 300mm
Thickness: 80mm
Edge detail: Pencil Edge Chamfer.
Finish: Washed /Cast
Shades: Supplied with three shade/texture variations to simulate the varied appearance of Natural Sandstone. Available in Buff and Grey.
Consult with the technical literature for details. We also provide a design and specification service and it is recommended that they are consulted early in the design process.

Manufacturer: Aggregate Industries, Hulland Ward, Ashbourne, Derbyshire DE6 3ET. Tel: 01335 372222. Fax: 01335 370074 Web: http://www.aggregate.com/commercial-hard-landscaping

Product reference: Stonemaster flag paving
Colour/ Finish: Three shade variation in both Buff and Grey
Edge detail: Pencil Edge Chamfer
Method of manufacture: Semi dry pressed and secondary processed.
Nominal sizes: 600 x 450mm / 450 x 450mm / 450 x 300mm

Manufacturer: Aggregate Industries, Hulland Ward, Ashbourne, Derbyshire DE6 3ET. Tel: 01335 372222. Fax: 01335 370074 Web: http://www.aggregate.com/commercial-hard-landscaping

Andover Textured Paving
A premium quality paving range manufactured from high quality granite aggregates and specially selected mica particles to provide a glinting appearance. 
The slabs are wet pressed and secondary processed. 
The pavings are designed for high volume pedestrian areas, town centres, shopping precincts, footway crossings and for areas subject to heavy vehicular traffic overrun.
Appalachian products comply with the strength and slip resistant requirements of BS EN 1339. 
Slip Resistance to BS EN 1339: Low.

Andover: Size: 400 x 400mm / 450 x 450mm / 600 x 600mm / 400x200
Thickness: 65mm / 70mm / 50mm
Edge detail: Chamfer / Square.
Finish: Textured 
Shades:
Light Grey. 
Silver Grey
Midnight Grey 
Silver Fleck

Cream

White

Chestnut

Oak

Consult with the technical literature for details. We also provide a design and specification service and it is recommended that they are consulted early in the design process.

Manufacturer: Aggregate Industries, Hulland Ward, Ashbourne, Derbyshire DE6 3ET. Tel: 01335 372222. Fax: 01335 370074 Web: http://www.aggregate.com/commercial-hard-landscaping

Product reference: Andover flag paving
Colour/ Finish: Light Grey / Eco Buff Fleck / Eco Grey Fleck  / Midnight Grey /Chestnut / Oak - Ground / Textured
Edge detail: Chamfer / Square.
Method of manufacture: Wet pressed and secondary processed.
Nominal sizes: 400 x 400 x 65mm / 450 x 450 x 67mm / 450 x 450 x 70mm / 600 x 600 x 50mm.

Appalachian Paving
A premium quality paving range manufactured from high quality granite aggregates and specially selected mica particles to provide a glinting appearance. 
The slabs are wet pressed and secondary processed. 
The pavings are designed for high volume pedestrian areas, town centres, shopping precincts, footway crossings and for areas subject to heavy vehicular traffic overrun.
Appalachian products comply with the strength and slip resistant requirements of BS EN 1339. 
Slip Resistance to BS EN 1339: Low.
Size: 400 x 400mm / 450 x 450mm / 600 x 600mm
Thickness: 65mm / 67mm / 50mm
Edge detail: Chamfer / Square.
Finish: Ground 
Shades:
Grey (ground )
Black Fleck ( ground ). 
Charcoal ( ground ).

Lemoor ( ground )

Consult with Charcon technical literature for details. Charcon can also provide a design and specification service and it is recommended that they are consulted early in the design process.

Manufacturer: Charcon, Hulland Ward, Ashbourne, Derbyshire DE6 3ET. Tel: 01335 372222. Fax: 01335 370074 Web: www.charcon.com  
Product reference: Appalachian flag paving
Colour/ Finish: Grey / Black Fleck / Charcoal / Lemoor- Ground

Edge detail: Chamfer / Square.
Method of manufacture: Wet pressed and secondary processed.
Nominal sizes: 400 x 400 x 65mm / 450 x 450 x 67mm / 600 x 600 x 50mm.

Ultrapave Paving
Ultrapave paving slabs incorporate fibre or steel reinforcement and specially selected aggregates and are designed for urban pavements, shopping precincts, footway crossings and areas subject to heavy vehicular traffic overrun. 
Ultrapave products comply with the strength and slip resistant requirements of BS EN 1339. 
Slip Resistance to BS EN 1339: Low.

Ultrapave: Size: 600 x 600mm / 600 x 450mm / 600 x 750mm.
Thickness: 63mm / 72mm
Edge detail: Square
Finish: Standard Pimple / Textured.
Shade: Standard Grey / Dark Grey / Silver Grey. 
Consult with the technical literature for details. We also provide a design and specification service and it is recommended that they are consulted early in the design process.

Manufacturer: Aggregate Industries, Hulland Ward, Ashbourne, Derbyshire DE6 3ET. Tel: 01335 372222. Fax: 01335 370074 Web: http://www.aggregate.com/commercial-hard-landscaping

Product reference: 
Ultrapave flag paving – Steel reinforced
Ultrapave flag paving – Fibre reinforced
Colour/ Finish: 
Dark Grey / Silver Grey – Textured Finish – for steel reinforced slabs.
Standard Grey – Pimple finish – for steel & fibre reinforced slabs.
Method of manufacture: Wet Pressed and Secondary Processed
Nominal sizes: 600 x 600mm / 600 x 450mm / 600 x 750mm - fibre reinforced standard grey.
600 x 600 and 600 x 450 Standard Grey steel reinforced.
600 x 600 and 600 x 750 Steel reinforced textured finish.

Moordale Paving
A high quality and cost effective paving range, manufactured from a combination of Limestone and Yorkstone aggregates, wet pressed and secondary processed. 
The pavings are designed for high volume pedestrian areas, town centres, shopping precincts, footway crossings and for areas subject to heavy vehicular traffic overrun.
Moordale products comply with the strength and slip resistant requirements of BS EN 1339. 
Slip Resistance to BS EN 1339: Low.

Moordale Size: 400 x 400mm / 450 x 450mm / 600 x 600mm
Thickness: 65mm / 70mm / 50mm / 60mm
Edge detail: Chamfer / Square.
Finish: Ground / Textured
Shades:
Grey (ground and textured) / Buff (ground and textured) .  Not all shades are available in all unit sizes.
50mm thick units are only suitable for high-volume pedestrian areas.
Consult with the technical literature for details. We also provide a design and specification service and it is recommended that they are consulted early in the design process.

Manufacturer: Aggregate Industries, Hulland Ward, Ashbourne, Derbyshire DE6 3ET. Tel: 01335 372222. Fax: 01335 370074 Web: http://www.aggregate.com/commercial-hard-landscaping

Product reference: Moordale flag paving
Colour/ Finish: Grey / Buff - Ground / Textured / French Grey - Textured
Edge detail: Chamfer / Chamferless
Method of manufacture: Wet pressed and secondary processed.
Nominal sizes: 400 x 400 x 50mm / 400 x 400 x 65mm / 450 x 450 x 70mm / 450 x 450 x 50mm / 600 x 600 x 50mm.

Courtstone Paving
Designed specifically to replicate natural Caithness stone paving, Courtstone’s riven profile is derived from natural stone masters. 
The pavings are designed for high volume pedestrian areas, town centres, shopping precincts, footway crossings and for areas subject to heavy vehicular traffic overrun.
Courtstone products comply with the strength and slip resistant requirements of BS EN 1339. 
Slip Resistance to BS EN 1339: Low.

Courtstone: Size: 450 x 450mm / 450 x 600mm / 600 x 600mm / 600 x 750mm / 600 x 900mm
Thickness: 63mm
Edge detail: Square.
Finish: Riven
Shades: Charcoal.
Consult with Charcon technical literature for details. Charcon can also provide a design and specification service and it is recommended that they are consulted early in the design process.

Manufacturer: Aggregate Industries, Hulland Ward, Ashbourne, Derbyshire DE6 3ET. Tel: 01335 372222. Fax: 01335 370074 Web: http://www.aggregate.com/commercial-hard-landscaping

Product reference: Courtstone flag paving
Colour/ Finish: Charcoal - Riven
Edge detail: Square.
Method of manufacture: Wet pressed 
Nominal sizes: 450 x 450 x 63mm / 450 x 600 x 63mm / 600 x 600 x 63mm / 600 x 750 x 63mm / 600 x 900 x 63mm

Academy Paving 
An affordable commercial paving that doesn’t compromise on aesthetics manufactured from local aggregates to manufacturing plants for a reduced carbon footprint. 
The slabs are wet pressed and secondary processed. The pavers are designed for high volume pedestrian areas, town centres, shopping precincts, footway crossings and for areas subject to heavy vehicular traffic overrun using the 400x400x65 size.
Academy paving complies with the strength and slip resistant requirements of BS EN 1339. 
Slip Resistance to BS EN 1339: Low.

Academy:  Size: 400 x 400mm / 450 x 450mm / 600 x 600mm
Thickness: 65mm / 70mm / 50mm
Edge detail:  Square.
Finish:  Textured 
Shades: Grey
Consult with Charcon technical literature for details. Charcon can also provide a design and specification service and it is recommended that they are consulted early in the design process.

Manufacturer: Aggregate Industries, Hulland Ward, Ashbourne, Derbyshire DE6 3ET. Tel: 01335 372222. Fax: 01335 370074 Web: http://www.aggregate.com/commercial-hard-landscaping

Product reference: Academy flag paving
Colour/ Finish: Grey Textured
Edge detail:  Square.
Method of manufacture: Wet pressed and secondary processed.
Nominal sizes: 400 x 400 x 65mm / 450 x 450 x 70mm / 600 x 600 x 50mm

British Standard Paving
Charcon manufacture a range of hydraulically pressed concrete paving slabs for use when standard paving is required. 
Click on the name below to jump to the product and specification details.
Paving BS EN 1339
Small Element

Paving BS EN 1339:
Charcon hydraulically pressed paving is available in 50mm and 63mm thicknesses.
Designed for high volume pedestrian areas, town centres, shopping precincts, footway crossings and for areas subject to heavy vehicular traffic overrun. 
The pavings comply with the strength and slip resistant requirements of BS EN 1339. 
Slip Resistance to BS EN 1339: Low.

BS EN 1339: Size: 450 x 600mm / 600 x 600mm / 600 x 750mm / 600 x 900mm.
Thickness: 50mm / 63mm. 
Edge detail: Square.
Finish: Standard / Hobnail / Barfaced
Shades: Grey / Buff / Red
NB. Non British Standard Paving sizes 37mm thick plus 600 x 300 50mm and 900 x 300 x 50mm are also available. 
Consult with the technical literature for details. We also provide a design and specification service and it is recommended that they are consulted early in the design process.

Manufacturer: Aggregate Industries, Hulland Ward, Ashbourne, Derbyshire DE6 3ET. Tel: 01335 372222. Fax: 01335 370074 Web: http://www.aggregate.com/commercial-hard-landscaping

Product reference: British Standard Paving
Colour/ Finish: Grey / Buff / Red - Standard / Hobnail / Barfaced. 
Edge detail: Square
Method of manufacture: Hydraulically pressed 
Nominal sizes: 
450 x 600 x 50mm / 450 x 600 x 63mm
600 x 600 x 50mm / 600 x 600 x 63mm
600 x 750 x 50mm / 600 x 750 x 63mm
600 x 900 x 50mm / 600 x 900 x 63mm

Small Elements
We manufacture a range of small element British Standard Paving units in a standard finish which combines aesthetic appeal with high load-bearing capabilities and low maintenance. 
Our small element paving is hydraulically pressed to the requirements of BS EN 1339, in plan sizes.

Small Element: Size: 300 x 300mm / 400 x 200mm / 400 x 400mm / 450 x 450mm / 450 x 300mm.
Thickness: 50 / 60 / 65 / 70mm
Edge detail: Chamfer.
Finish: Standard 
Shades: Grey / Buff / Red.
We also manufacture a range of dished and fluted paving slabs in addition to a cycle demarcation block.
Consult with the technical literature for details. We also provide a design and specification service and it is recommended that they are consulted early in the design process.

Manufacturer: Aggregate Industries, Hulland Ward, Ashbourne, Derbyshire DE6 3ET. Tel: 01335 372222. Fax: 01335 370074 Web: http://www.aggregate.com/commercial-hard-landscaping

Product reference: British Standard Paving - Small Element
Format: Plain / Dished / Fluted / Cycle Demarcation Block.
Colour/ Finish: Grey / Buff / Red
Not all units available in all colours. Consult with us for details.
Edge detail: Chamfer
Method of manufacture: Hydraulically pressed 
Nominal sizes:
Small units:
300 x 300 x 60mm
400 x 400 x 50mm / 400 x 400 x 65mm
450 x 450 x 50mm / 450 x 450 x 70mm
450 x 300 x 65mm.
Dished / Fluted:
600 x 600 x 63mm
Cycle Demarcation Block
198 x 150 x 95mm / 914 x 150 x 95mm

Tactile Paving
A range of paving designed specifically to meet the Department of the Environment, Transport and Regions ‘Guidance on the Use of Tactile Paving Surfaces’. Tactile paving products comply with the requirements of BS EN 1339.

Tactile: Size: 400 x 400 x 50mm / 400 x 400 x 65mm / 450 x 450 x 50mm / 450 x 450 x 70mm.
Edge detail: Square.
Finish: Blister / Hazard Warning / Platform Edge Warning (offset blister) / Platform Edge Warning (lozenge) / Guidance / Cycleway 
Shades: Grey / Buff /Red
Consult with the technical literature for details. We also provide a design and specification service and it is recommended that they are consulted early in the design process.

Manufacturer: Aggregate Industries, Hulland Ward, Ashbourne, Derbyshire DE6 3ET. Tel: 01335 372222. Fax: 01335 370074 Web: http://www.aggregate.com/commercial-hard-landscaping

Product reference: 
Tactile Paving – Hazard warning
Tactile Paving – Blister
Tactile Paving – Guidance
Tactile Paving – Platform edge (offset blister)
Tactile Paving – Platform edge (lozenge)
Tactile Paving – Cycleway
Colour/ Finish: 
Hazard warning:
Buff – Stock colour for 400 x 400 x 50mm
Grey / Red – To order colour for 400 x 400 x 50mm
Buff / Grey / Red – To order colour for 400 x 400 x 65mm
Blister:
Buff / Grey / Red – Stock colour for 400 x 400 x 50mm, 400 x 400 x 65mm
Buff / Red – Stock colour for 450 x 450 x 50mm
Grey – To order colour for 450 x 450 x 50mm
Buff / Grey / Red – To order colour for 450 x 450 x 70mm
Guidance:
Buff / Grey – Stock colour for 400 x 400 x 50mm
Red – To order colour for 400 x 400 x 50mm
Buff / Grey / Red – To order colour for 400 x 400 x 65mm
Platform edge (offset blister):
Buff – Stock colour for 400 x 400 x 50mm
Grey / Red – To order colour for 400 x 400 x 50mm
Buff / Grey / Red – To order colour for 400 x 400 x 65mm
Platform edge (lozenge):
Buff – Stock colour for 400 x 400 x 50mm
Grey / Red – To order colour for 400 x 400 x 50mm
Cycleway:
Buff / Grey – Stock colour for 400 x 400 x 50mm
Red – To order colour for 400 x 400 x 50mm
Buff / Grey / Red – To order colour for 400 x 400 x 65mm
Method of manufacture: Hydraulically pressed 
Nominal sizes: 
400 x 400 x 50mm / 400 x 400 x 65mm
450 x 450 x 50mm / 450 x 450 x 70mm.

Elite Format 3 Paving
A deterrent paving for all environments in which pedestrian or vehicular traffic needs to be discouraged. 
The paving is wet cast in moulds with formers and incorporating white cement for high visibility. 
Elite Format 3 complies with the performance levels in BS EN 1339. 
Consult with the technical literature for details. We also provide a design and specification service and it is recommended that they are consulted early in the design process..

Manufacturer: Aggregate Industries, Hulland Ward, Ashbourne, Derbyshire DE6 3ET. Tel: 01335 372222. Fax: 01335 370074 Web: http://www.aggregate.com/commercial-hard-landscaping

Product reference: Elite Format 3 Deterrent Paving.
Colour/ Finish: White.
Method of manufacture: Wet cast
Nominal sizes: 600 x 600 x 74mm.