Q10 KERBS/ EDGES/ CHANNEL/ PAVING ACCESSORIES

110 PROPRIETARY PRECAST CONCRETE

Charcon manufacture a range of precast concrete kerbs.

EcoKerb

Countryside Kerb

K-Lite™ Kerbs

Cairnhill Kerb

Access Kerb

British Standard Kerbs

EcoKerb
The Charcon Eco Range has been developed to make a positive contribution to sustainable construction by maximising resource productivity. 
The factory utilises advanced equipment to meet high environmental standards.
Charcon’s range of EcoPave and EcoKerb products uses secondary and recycled materials in the manufacture of it’s precast concrete units. The only virgin resource used in the product is cement and even this has been partially substituted with recycled materials. 
Click on the name below to jump to the product and specification details.
EcoKerb Classic
EcoKerb Classic Wide Top

EcoKerb Classic
A square-edge profile kerb.
Size:
145 x 255 x 914mm Straight
145 x 150 x 914mm Crossing
LH/RH Droppers
Radius (1.8m, 3m, 6m and 9m - external only)
Quadrant 305mm
Consult with Charcon technical literature for details. Charcon can also provide a design and specification service and it is recommended that they are consulted early in the design process.

110 PROPRIETARY PRECAST CONCRETE KERBS
Standard: ToBS EN 1340
Manufacturer: Charcon, Hulland Ward, Ashbourne, Derbyshire DE6 3ET. Tel: 01335 372222. Fax: 01335 370074 Web: www.charcon.com 
Product reference: EcoKerb Classic

Size (width x height x length): 145 x 255 x 914 mm Straight

Special shapes: 
Crossing - 145 x 150 x 914mm
LH/RH Droppers
Radius (1.8m, 3m, 6m and 9m - external only).
Quadrant 305mm.
Flat Top Edging: 50 x 150 x 914mm Square

Finish: Textured

Colour: Black Fleck.

EcoKerb Classic Wide Top
A wide top kerb.
Size:
205 x 290 x 914mm Straight
100 x 290 x 914mm Crossing
LH/RH Droppers
Radius (3m, 6m and 9m - external only)
Consult with Charcon technical literature for details. Charcon can also provide a design and specification service and it is recommended that they are consulted early in the design process.

110 PROPRIETARY PRECAST CONCRETE KERBS
Standard: To BS EN 1340
Manufacturer: Charcon, Hulland Ward, Ashbourne, Derbyshire DE6 3ET. Tel: 01335 372222. Fax: 01335 370074 Web: www.charcon.com 
Product reference: EcoKerb Classic Wide Top

Size (width x height x length): 205 x 290 x 914mm Straight

Special shapes: 
Crossing - 100 x 290 x 914mm
LH/RH Droppers
Radius (3m, 6m and 9m - external only).
Flat Top Edging: 50 x 150 x 914mm Square

Finish: Textured

Colour: Black Fleck

Countryside Kerb
A natural rough-hewn appearance, designed to enable the kerb to blend in particularly well in traditional or conservation environments. 
Two product options provide a choice of aggregate bases, shades and installed profiles. 
Click on the name below to jump to the product and specification details.
Countryside Classic Kerb
Countryside Classic Wide Top Kerb

Countryside Classic Kerb
A textured kerb with exposed Cornish granite aggregate, giving it a weathered natural look. Available in standard kerb profiles with a full range of accessories.
Sizes: 125 x 255 x 914mm Half Battered / 145 x 255 x 914mm Square.
Profile: Half-batter/ Square
Finish: Textured
Colour: Silver Grey
Trafficking: Designed to withstand occasional impact
Consult with Charcon technical literature for details. Charcon can also provide a design and specification service and it is recommended that they are consulted early in the design process.

110 PROPRIETARY PRECAST CONCRETE KERBS
Standard: To BS EN 1340
Manufacturer: Charcon, Hulland Ward, Ashbourne, Derbyshire DE6 3ET. Tel: 01335 372222 Fax: 01335 370074 Web: www.charcon.com  
Product reference: Countryside Classic Kerb

Size (width x height x length): 125 x 255 x 914mm Half Battered / 145 x 255 x 914mm Square

Special shapes:
Crossing units: 
Bullnose - 125 x 150 x 914mm.
Square - 145 x 150 x 914mm.
Radius units: 
Half Battered -125 x 255mm.
Square - 145 x 255mm. 
Radius units available in 1.8, 3, 6 and 9 metre external radius versions
Dropper units: 
Half Battered - 125 x 255-150 x 914mm.
Square - 145 x 255-150 x 914mm.
Quadrant: 
Half Battered - R305 x 255mm.
Square - R305 x 255mm.
Internal Angles: 
Half Battered - 125 x 255mm.
External Angle:
Half Battered - 125 x 255mm.
Flat Top Edging: 
Square - 50 x 150 x 914mm.

Finish: Textured

Colour: Silver Grey

Countryside Classic Wide Top Kerb
A textured version of the standard kerb in a wide top profile, available with a range of accessories.
Sizes: 290 x 205 x 914mm
Profile: Square
Finish: Textured
Colour: Silver Grey
Trafficking: Designed to withstand occasional impact
Consult with Charcon technical literature for details. Charcon can also provide a design and specification service and it is recommended that they are consulted early in the design process.

110 PROPRIETARY PRECAST CONCRETE KERBS
Standard: To BS EN 1340
Manufacturer: Charcon, Hulland Ward, Ashbourne, Derbyshire DE6 3ET. Tel: 01335 372222. Fax: 01335 370074 Web: www.charcon.com 
Product reference: Countryside Classic Wide Top Kerb

Size (width x height x length): 290 x 205 x 914mm

Special shapes:
Crossing units: 
Wide Top - 290 x 100 x 914mm 
Radius units:
Wide Top - 290 x 205mm
Radius units available in 3, 6 and 9 metre external radius versions
Dropper units: 
Wide Top - 290 x 205-100 x 914mm.

Finish: Textured

Colour: Silver Grey

Cairnhill Kerb
Cairnhill kerbs have been designed specifically to replicate natural Whin kerbs.
Sizes: 125 x 255 x 914mm / 125 x 150 x 914mm
Profile: Square
Finish: Riven
Colour: Charcoal
Trafficking: Designed to withstand occasional impact
Consult with Charcon technical literature for details. Charcon can also provide a design and specification service and it is recommended that they are consulted early in the design process.

110 PROPRIETARY PRECAST CONCRETE KERBS
Standard: To BS EN 1340.
Manufacturer: Charcon, Hulland Ward, Ashbourne, Derbyshire DE6 3ET. Tel: 01335 372222. Fax: 01335 370074 Web: www.charcon.com 
Product reference: Cairnhill Kerbs

Size (width x height x length): 125 x 255 x 914mm / 125 x 150 x 914mm

Special shapes: Not available

Finish: Riven.

Colour: Charcoal.

K-Lite™ Traditional Kerbs
A split stone reproduction of natural granite similar to Countrysetts. 
Manufactured with a weathered top edge and are available in two colours.
The kerbs are manufactured from South West Granites using a wet pressed method, with the kerb split and shot blasted to expose the aggregate.
Sizes: 100 x 140 x 440mm / 100 x 215 x 290mm
Profile: Bull Nose / Split.
Finish/ Texture: Weathered top edge / Split Finish Face
Shades: Dark Grey / Silver Grey.
Trafficking: Designed to withstand occasional impact
Consult with Charcon technical literature for details. Charcon can also provide a design and specification service and it is recommended that they are consulted early in the design process.

110 PROPRIETARY PRECAST CONCRETE KERBS
Standard: To BS EN 1340.
Manufacturer: Charcon, Hulland Ward, Ashbourne, Derbyshire DE6 3ET. Tel: 01335 372222. Fax: 01335 370074 Web: www.charcon.com 
Product reference: K-Lite™ Traditional Kerbs

Size (width x height x length): 100 x 140 x 440mm / 100 x 215 x 290mm

Special shapes: Not available

Finish: Weathered top edge / Split face finish.

Colour: Dark Grey / Silver Grey

Access Kerb
Access kerb is available in height and profile options to permit level entry access to standard or guided buses. Designed with an integral marker bump to assist the bus driver to position the bus platform immediately adjacent to the kerb. Available in a Standard Profile, with or without, an integral marker bump and a Guided Bus profile. Both, with a comprehensive range of transition units and accessories.
Access kerb is also available in natural granite to order. Consult with Charcon for recommendations and details.                                                                                   
Size:
Standard profile – 323 x 350 x 1000mm (220mm Kerb Height, with marker bump), 271 x 350 x 1000mm (220mm Kerb Height, without marker bump), 310 x 310 x 1000mm (180mm Kerb Height, with marker bump), 276 x 290 x 1000mm (160mm Kerb Height, with marker bump), 224 x 290 x 1000mm (160mm Kerb Height, without marker bump). 
Installed Edge Profile - Low Splay.
Guided Bus profile – 260 x 310 x 1000mm (180mm Kerb Height no marker bump). 
Installed Edge Profile - Low Splay 
Finish/ Texture: Standard
Shades: Grey
Trafficking: Designed to withstand occasional bus impact
Consult with Charcon technical literature for details. Charcon can also provide a design and specification service and it is recommended that they are consulted early in the design process.

110 PROPRIETARY PRECAST CONCRETE KERBS
Standard: To BS EN 1340
Manufacturer: Charcon, Hulland Ward, Ashbourne, Derbyshire DE6 3ET. Tel: 01335 372222. Fax: 01335 370074 Web: www.charcon.com 
Product reference: Access Kerbs - Standard profile / Guided Bus Profile

Size (width x height x length):
Standard profile – 323 x 350 x 1000mm (220mm Kerb Height, with marker bump), 271 x 350 x 1000mm (220mm Kerb Height, without marker bump), 310 x 310 x 1000mm (180mm Kerb Height, with marker bump), 276 x 290 x 1000mm (160mm Kerb Height, with marker bump), 224 x 290 x 1000mm (160mm Kerb Height, without marker bump). 
Guided Bus profile – 260 x 310 x 1000mm (180mm Kerb Height no marker bump).

Special shapes:
Dropper Units: Standard Profile
220-160 x 1000mm / 180-125 x 1000mm / 160-125 x 1000mm
Dropper Units: Guided Bus Profile. 
180-125 x 1000mm

Finish: Standard

Colour: Grey

British Standard Kerbs
Charcon produce a range of kerbs and channels as specified in the current version of BS EN 1340. 
All straight units and the majority of radius units are hydraulically pressed, other radius units are hammer-compacted. 
All straight kerbs listed are 914mm standard lengths. The 125 x 255 HB2 is also available in 609mm lengths. 
Consult with Charcon technical literature for details. Charcon can also provide a design and specification service and it is recommended that they are consulted early in the design process.

110 PROPRIETARY PRECAST CONCRETE KERBS
Standard: To BS EN 1340.
Manufacturer: Charcon, Hulland Ward, Ashbourne, Derbyshire DE6 3ET. Tel: 01335 372222. Fax: 01335 370074 Web: www.charcon.com  
Product reference: British Standard Kerbs

Size (width x height x length):
150 x 305 x 914mm HB 1
125 x 255 x 914mm HB 2
125 x 150 x 914mm HB 3
255 x 125 x 914mm CS1
150 x 125 x 914mm CS 2
125 x 255 x 914mm SP
125 x 150 x 914mm BN.
125 x 255 x 609mm HB 2.

Special shapes:
Droppers and Crossing kerbs:
125mm x 255mm HB – 125mm x 150mm BN (LH) DL1.
125mm x 255mm HB – 125mm x 150mm BN (RH) DR1.
125mm x 255mm SP – 125mm x 150mm BN (LH) DL2.
125mm x 255mm SP – 125mm x 150mm BN (RH) DR2.
125mm x 150mm BN As crossing kerb.
125mm x 255mm BN – 125mm x 150mm BN (LH) Non-BS.
125mm x 255mm BN – 125mm x 150mm BN (RH) Non–BS.
Radius Droppers BS EN 1340:
125mm x 255mm HB – 125mm x 150mm BN (LH).
125mm x 255mm HB – 125mm x 150mm BN (RH).
Available in 4, 5, 6, 8 and 10m.
Radius Kerbs and Channels: Refer to Charcon Technical Department for details.
Quadrants: BS EN 1340
305mm x 255mm QHB / 455 x 255mm QHB / 305 x 255mm QSP / 305 x 255mm QBN.
Transition Kerbs: BS EN 1340
125mm x 255mm HB RH – 125mm X 255mm SP LH TR.
125mm x 255mm HB LH – 125mm X 255mm SP RH TL.
Angles: BS EN 1340
125mm x 255mm HB Ext Angle HBXA.
125mm x 255mm SP Ext Angle SPXA.
125mm x 255mm HB Internal Angle HBIA.
125mm x 255mm SP Internal Angle SPIA.
Non-Standard Kerbs:
150mm x 305mm BN / 125mm x 255mm BN / 150mm x 125mm HB.
Non-Standard Channels:
150mm x 150mm CS / 150mm x 100mm CS.
Non-Standard Droppers and Crossing Kerbs:
125mm x 255mm HB – 125mm x 175mm SP (LH) DL.
125mm x 255mm HB – 125mm x 175mm SP (RH) DR.
125mm x 175mm SP as Crossing Kerb.
Double Pattern:
Code WR1 - 125mm x 255mm HB – 125mm x 215mm WRCC (LH).
Code WR2 - 125mm x 215mm HB – 125mm x 175mm WRCC (LH).
Code WR3 - 125mm x 215mm HB – 125mm x 175mm WRCC (RH).
Code WR4 - 125mm x 255mm HB – 125mm x 215mm WRCC (RH).

Finish: Standard.

Colour: Grey.